Oblig 3 – Signals, Variables and Process Sensivity

Task a:
Upon simulating the entity delay, we see that the signal of out_data is not updated until after 450 ns have passed. The main reason for this so called ‘delay’ in the change of the signal is caused by the rules according to which signals are updated in simulation in VHDL. One of those rules clearly states that signals are updated once in a process invocation, and only at the exit of a process. If we inspect the sensivity list of the delay entity and its testbench, we see that a new process is triggered by the changes to either the clock signal mclk or the reset signal rst_n. For the first 100 ns rst_n holds the value ‘0’, before chaning to ‘1’ , meaning that upon the exit of the second process, signals data1, data3 and data5, and variables data2 and data4 are no longer assigned value ‘00000000’. The process then runs for another 100 ns before indata changes to ‘11111111’, but the clock signal is on the falling egde at this particular moment, meaning that the simulation has to run for another 50 ns before any changes to data1 signal can be applied. Upon reaching the 250 ns marker, a simultanous assignment of values takes place in the simulation, where signal data1 is assigned the value of indata, and variable data2 is assigned the value of data1. Then at 350 ns, at the exit of the seventh process, signal data3 receives the value stored in variable data2, and variable data4 is given the value of data3. Finally, after 450 ns, at the exit of the ninth process, the value of variable data4 is assigned to signal data5 at the rising edge of the clock, and the value is then given to out_data.

Task b:
After applying the changes to both the enitity delay and its testbench tb_delay, the out_data signal is undefind for the first 50 ns, because all variables have been replaced with signals. This means that any update to any singal in the simulation will happen at the exit of a process, and not immediately as is the case for variables. Hence, since the first process exits at 50 ns, the out_data signal will remain undefined for the duration od the first process. The next change in the out_data happens at 750 ns, because the first change in in_data does not happen until after 300 ns have passed. This change is, however, applied at the falling edge of the clock, hence the new value of in_data is assigned to data1 signal at the exit of the seventh process, when the clk is at the rising egde again. Since the process only contains signals, the value of in_data assigned to data1 will be assigned to each consecutive data signal after 100 ns. This means that it will take 400 ns before the value of in_data will show in the out_data. This is also true for the change in in_data at 450 ns, when in_data receives the value “00001111”, which is visible at the output at 850 ns (the last change in out_data).

Task c:
In the case presented in this task, the entity variabled_vs_signals has a sensitivity list which contains the signals indata, sig1 and sig2, meaning that a process will be triggered be the change of one or more of those signals . If we inspect the process in the architecture of the entity, we will see that all the signals are updated in parallell. In a situation like that the last assignment of values is the valid one, meaning that in our case, sig1 will be changed to not var1, while sig2 will receive value not indata. Signal outdata(3 downto 2) will be updated to value ‘10’ at the exit of the process, which is the same value as outdata(7 downto 6) receives. This happens because both values are assigned value sig2 & sig1. The value of signal outdata(5 downto 4) is however opposite of the value of outdata(1 downto 0), because both signals receive values built from variable values. It is common knowlegde that variables are updated immediately, without being dependant on the process. This simply means that the when the variables var1 and var2 are changed to not values of themselves, these opposite values will be assigned to each of the respective sub-vectors of the signal outdata.

Task d:
The value of outdata(7 downto 6) and outdata(3 downto 2) differ from those in task c, because the removal og signal sig1 and sig2 leads to the invocation of a new process only when a change is applied to the indata signal. So when the simulation starts, both outdata sub-vectors will be undefined for teh first 100 ns, until indata receives value ‘1’. The values of outdata(7 downto 6) and outdata(3 downto 2) will be then the same as during the first 100 ns of the simulation in task c.